## Slide 1: Graceful Degradation on FPGAs: A High-Radix Online Approach
  Motivation
Joshua Laney
    The key to online arithmetic is redundancy, allowing MSDs to be guessed and LSDs to correct for error
  Degradation Data
    FPGAs are configurable but have an unchangeable microarchitecture targeting LSD-first operation
    In some applications accuracy is forfeited in the pursuit of speed
    Online arithmetic leads to graceful degradation due to MSD-first carry chains
  Does high-radix online arithmetic perform better than radix-2 on FPGAs?
Image adapted from Digital Arithmetic textbook by Milos Ercegovac
Image adapted from Kan Shi’s PhD Thesis
  Implementation
  Testing
    Addition is done fully in parallel with a constant carry chain
    The test bench must withstand higher frequencies than the DUT
  Speed Data
    Radix-2 is generally faster than higher radices, especially in the multiplier
    Radix-4 adders degrade more advantageously than radix-2
    This is not the case for multipliers or higher radices
  Only radix-4 addition benefits from the FPGA microarchitecture over radix-2
    Multiplication works through an iterative residual approach, and is pipelined
Image taken from Intel